## Slide 1: Multimedia Systems and Applications
Lecture 2 - Sound/Audio

## Slide 2: Objectives
To understand how computers process sound.
To understand how computers synthesize sound.
To understand the differences between two major kinds of audio, namely digitized sound and MIDI music.

## Slide 3: Contents
The Nature of Sound
Computer Representation of Sound
Computer Music — MIDI
Summary —MIDI versus digital audio
Exercises

## Slide 4: The Nature of Sound
Sound is a physical phenomenon produced by the vibration of matter and transmitted as waves.

## Slide 5: The Nature of Sound
However, the perception of sound by human beings is a very complex process. It involves three systems:
  The source which emits sound;
  The medium through which the sound propagates;
  The detector which receives and interprets the sound.

## Slide 6: The Nature of Sound
Sounds we heard everyday are very complex.
Every sound is comprised of waves of many different frequencies and shapes. But the simplest sound we can hear is a sine wave.
Sound waves can be characterized by the following attributes:
Period, Frequency, Amplitude, Bandwidth,
Pitch, Loudness, Dynamic.

## Slide 7: The Nature of Sound

## Slide 8: Pitch and Frequency
Period is the interval of time at which a periodic signal repeats regularly.
Pitch is a perception of sound by human beings. It measures the feeling of the sound as it is perceived by a listener.
A bird makes a high pitch. A lion makes a low pitch.
Frequency measures a physical property of a wave. It is the reciprocal value of period f =1/P. The sensation of a frequencies is commonly referred to as the pitch of a sound.
The unit is Herts (Hz) or kiloHertz (kHz).
Notes: Pitch حدة الصوت

## Slide 9: Pitch and Frequency

## Slide 10: Loudness and Amplitude
The other important perceptual quality is loudness or volume.
Amplitude is the measure of sound levels.
For a digital sound, amplitude is the sample value.
The reason that sounds have different loudness is that they carry different amount of power.

## Slide 11: Loudness and Amplitude
The unit of power is watt. The intensity of sound is the amount of power transmitted through an area of 1 m2 oriented perpendicular to the propagation direction of the sound.
If the intensity of a sound is 1 watt/m2, we may start feel the sound. The ear may be damaged. This is known as the threshold of feeling.
Notes: Intensity: شدة

## Slide 12: Loudness and Amplitude
If the intensity is 10 -12 watt/m2, we may just be able to hear it. This is know as the threshold of hearing.
The relative intensity of two different sounds is measured using the deciBel (dB).
Very often, we will compare a sound with the threshold of hearing.

## Slide 14: Dynamic and Bandwidth
Dynamic range means the change in sound levels.
For example, a large orchestra can reach 130dB at its climax and drop to as low as 30dB at its softest, giving a range of 100dB.
Bandwidth is the range of frequencies a device can produce or a human can hear.
Notes: Orchestra: أوركسترا
100/8=12.5

## Slide 15: Dynamic and Bandwidth

## Slide 16: Computer Representation of Sound
Sound waves are continuous while computers are good at handling discrete numbers.
In order to store a sound wave in a computer, samples of the wave are taken.
Each sample is represented by a number, the ‘code’.
This process is known as digitization.
This method of digitizing sound is know as pulse code modulation (PCM).

## Slide 17: Computer Representation of Sound
According to Nyquist sampling theorem, in order to capture all audible frequency components of a sound, i.e., up to 20kHz, we need to set the sampling to at least twice of this.
This is why one of the most popular sampling rate for high quality sound is 44,100 sample/sec.
Another aspect we need to consider is the resolution (Quantization bands), i.e., the number of bits used to represent a sample.
Often, 16-bits are used for each sample in high quality sound.

## Slide 18: Quality versus File Size
The size of a digital recording depends on the sampling rate, resolution and number of channels.
S = R  (b/8)  C  D
S file size bytes
R sampling rate (samples / second)
b resolution bits
C channels 1 - mono, 2 - stereo
D recording duration seconds

## Slide 21: Quality versus File Size
Higher sampling rate, higher resolution gives higher quality but bigger file size.
For example, if we record 10 seconds of stereo music at 44.1kHz, 16 bits, the size will be:
S = 44100  (16/8)  2  10
= 1,764,000 bytes
= 1722.7 Kbytes
= 1.68 Mbytes
High quality sound files are very big, however, the file size can be reduced by compression.

## Slide 22: File size for some common sampling rates and resolutions

## Slide 23: File size for some common sampling rates and resolutions

## Slide 24: Audio File Formats
The most commonly used digital sound format in Windows systems is .wav files.
Sound is stored in .wav as digital samples known as Pulse Code Modulation (PCM).
Each .wav file has a header containing information of the file.
  type of format, e.g., PCM or other modulations
  size of the data
  number of channels
  samples per second
  bytes per sample
There is usually no compression in .wav files.
Other format may use different compression technique to reduce file size.
.vox use Adaptive Delta Pulse Code Modulation (ADPCM).
.mp3 MPEG-1 layer 3 audio.
RealAudio file is a proprietary format.

## Slide 25: Some common audio files formats
Notes: An Internet media type,[1] originally called a MIME type after MIME and sometimes a Content-type after the name of a header in several protocols whose value is such a type, is a two-part identifier for file formats on the Internet.

## Slide 26: Audio Hardware
Recording and Digitizing sound:
  An analog-to-digital converter (ADC) converts the analog sound signal into digital samples.
  A digital signal processor (DSP) processes the sample, e.g. filtering, modulation, compression, and so on.
Play back sound:
  A digital signal processor processes the sample, e.g. decompression, demodulation, and so on.
  An digital-to-analog converter (DAC) converts the digital samples into sound signal.
All these hardware devices are integrated into a few chips on a sound card.

## Slide 27: Audio Hardware
Different sound card have different capability of processing digital sounds.
When buying a sound card, you should look at:
  maximum sampling rate.
  stereo or mono.
  duplex or simplex.

## Slide 28: Audio Software
Windows device driver — controls the hardware device.
Device manager — the user interface to the hardware for configuring the devices.
  You can choose which audio device you want to use.
  You can set the audio volume.

## Slide 29: Audio Software

## Slide 30: Audio Software
Mixer — its functions are:
  To combine sound from different sources.
  To adjust the playback volume of sound sources.
  To adjust the recording volume of sound sources.
Recording — Windows has a simple Sound Recorder.
Editing — The Windows Sound Recorder has a limiting editing function, such as changing volume and speed, deleting part of the sound.
There are many freeware and shareware programs for sound recording, editing and processing.
Notes: Sound processing Project
Sound Filters
Sound Effects
.WAV
.MP3
.MIDI

## Slide 31
Computer Music MIDI

## Slide 32: Computer Music (MIDI)
Sound waves, whether occurred natural or man-made, are often very complex, i.e., they consist of many frequencies.
Digital sound is relatively straight forward to record complex sound. However, it is quite difficult to generate (or synthesize) complex sound.
There is a better way to generate high quality music. This is known as MIDI — Musical Instrument Digital Interface.

## Slide 33: Computer Music (MIDI)
It is a communication standard developed in the early 1980s for electronic instruments and computers. It specifies the hardware connection between equipments as well as the format in which the data are transferred between the equipments.
Common MIDI devices include electronic music synthesizers, modules.

## Slide 34: General MIDI
General MIDI is a standard specified by MIDI Manufacturers Association. To be GM compatible, a sound generating device must meet the General MIDI system level-1 performance requirement:
  Minimum of 24 fully voices
  16 channels
  Minimum 16 simultaneous and different timbre instruments
  Minimum 128 preset instruments (MIDI program numbers)
  Support certain controllers
http://www.midi.org/techspecs/gm.php
http://en.wikipedia.org/wiki/General_MIDI
Notes: Timbre (“sound color”, or instrument, e.g., flute, cello, …)
In music, timbre (pronounced /ˈtam-bər'/, tɪm.bər like timber, or ˈtæm(brə),[1] from Fr. timbre tɛ̃bʁ) is the quality of a musical note or sound that distinguishes different types of sound production, such as voices or musical instruments. The physical characteristics of sound that mediate the perception of timbre include spectrum and envelope. Timbre is also known in psychoacoustics as sound quality or sound color.
For example, timbre is what, with a little practice, people use to distinguish the saxophone from the trumpet in a jazz group, even if both instruments are playing notes at the same pitch and amplitude. Timbre has been called "the psychoacoustician's multidimensional wastebasket category" [2] as it can denote many apparently unrelated aspects of a sound.

## Slide 35: MIDI Hardware
An electronic musical instrument or a computer which has MIDI interface should has one or more MIDI ports. The MIDI ports on musical instruments are usually labeled with:
  IN — for receiving MIDI data;
  OUT — for outputting MIDI data that are generated by the instrument;
  THRU — for passing MIDI data coming from IN to the next instrument.
MIDI devices can be daisy-chained together.

## Slide 36: MIDI Hardware

## Slide 37
MIDI Daisy-chain Network
IN
OUT
THRU
IN
THRU
IN
MIDI
USB
Notes: <number>
<footer>
<header>
<date/time>

## Slide 39
Multi-port MIDI Interface (2 in/out pairs)
IN
A B
OUT
A B
USB port
Thru switch – connects In to Out,
for use without a computer
Leave in ‘out’ position!
Lights!
Notes: <number>
<footer>
<header>
<date/time>

## Slide 40
Multi-port MIDI Interface (8 in/out pairs)
Front
Back
MIDI Outputs
MIDI Inputs
USB port
Notes: <number>
<footer>
<header>
<date/time>

## Slide 41: MIDI Data
Unlike digital sound, MIDI data does not encode individual samples. MIDI data encode musical events and commands to control instruments.
MIDI data are grouped into MIDI messages. Each MIDI message represents a musical event, e.g., pressing a key, setting a switch or adjusting foot pedals.
A sequence of MIDI messages is grouped into a track.

## Slide 42: MIDI Files
When using computers to play MIDI music, the MIDI data are often stored in MIDI files. Each MIDI files contains a number of chunks. There are two types of chunks:
  Header chunk — contains information about the entire file: the type of MIDI file, number of tracks and the timing.
  Track chunk — the actual data of MIDI track.

## Slide 43: MIDI music
Musical instruments are tuned to produce a set of fixed pitches.
Octave (0.125)

## Slide 44: Octave
For example, any two sounds whose frequencies make a 2:1 ratio are said to be separated by an octave and result in a particularly pleasing sound when heard.
Similarly two sounds with a frequency ratio of 5:4 are said to be separated by an interval of a third; such sound waves also sound good when played together.
Interval | Frequency Ratio | Examples
Octave | 2:1 | 512 Hz and 256 Hz
Third | 5:4 | 320 Hz and 256 Hz
Fourth | 4:3 | 342 Hz and 256 Hz
Fifth | 3:2 | 384 Hz and 256 Hz

## Slide 45: MIDI File
Music produced my musical instruments can be stored as codes since it produces discrete number of sounds (no. of keys).
For a piano of 12 sounds (12 keys):
- Code 0-11 (position of a key) : 1 byte
- Octave 0-7 (principle sounds): 1 byte
- Duration of using a key: 1 byte
For a key press it needs 3 bytes.
For 20 press/sec: 20 press * 3 bytes/press = 60 bytes/sec

## Slide 46: How MIDI Sounds Are Synthesized
A simplistic view is that:
The MIDI device stores the characteristics of sounds produced by different sound sources.
The MIDI messages tell the device which kind of sound, at which pitch is to be generated, how long the sound is played and other attributes the note should have.

## Slide 47: How Sounds Are Synthesized
There are two ways of synthesizing sounds:
FM Synthesis (Frequency Modulation)—Using one sine wave to modulate another sine wave, thus generating a new wave which is rich in timbre. It consists of the two original waves, their sum and difference are harmonics. The drawbacks of FM synthesis are: the generated sound is not real; there is no exact formula for generating a particular sound.
Wave-table synthesis— It stores representative digital sound samples. It manipulates these sample, e.g., by changing the pitch, to create the complete range of notes.

## Slide 48: FM Synthesis

## Slide 49: MIDI versus digital audio

## Slide 50: Exercises